F -107  FOAM  PARK  JET

Basic build guide to help assemble an rc park flyer

built from Dow Bluecore or Depron foam.

Glue single ½”wide strips

along bottom and top of

forward fuselage on both

sides. Use a triple wide strip

(3 strips glued together) for

the section below the intake

base and a double wide

strip for the top of the aft

fuselage on both sides.

Glue all canopy and nose

cone pieces together.

Bluecore note:

lightly cut and peel off a ¼”

wide section of the plastic

film from all edges where

corner strips will be glued.

This will keep it from

being in the way when

sanding to shape later.

Glue one fuselage side to

fuse bottom. Notch out

strips on forward fuse for

former 1.

Bluecore note:

lightly cut and peel off a ¼”

wide section of the plastic

film from all edges on fuse

bottom.

Glue formers F1, F2, F3

and F4 in place.

Glue other fuse side into

Place.

Glue fuse top front piece

into place.

Bluecore note: peel

plastic film from both

sides of this piece

before gluing.

Test fit canopy. Trim as

need for a tight fit.

Glue on intake base and

Nosecone.

Bluecore note: peel

plastic film from both

sides of these pieces

before gluing.

Sand forward fuse with

nosecone and canopy to

initial shape. Careful

not to sand too much

from the intake base

or the bottom of the fuse

yet.

Sand down fuselage

sides around the gun

pods to a smooth

finish.

Continue sanding to this

Shape. Test fit the

intake mount  piece

while sanding to know

how far up on the intake

base to shape.

Glue on the intake mount.

Assemble intake bottom,

sides and center piece.

Bluecore note: leave

plastic film on all interior

sides of the intake for a

smoother finish.

Glue intake to fuselage on

top of the intake mount.

Add  ½” strips to the upper inside edge of both intake sides as shown.

Glue together the two

motor mounts. Install the

3/8” sq hardwood with

epoxy. Then glue the

whole assembly to the

rear base of the fuse

bottom with epoxy.

Note: This mount can be

modified to fit a motor of

your choice.

Install hardware for

stabilizers. Cut two 1”sq

ply supports, two small

bearings from aluminum

tube. One control horn, one end stop bearing and an 8” piece of carbon rod that fits smoothly in the aluminum bearings.

Glue on the 1” plywood

supports to each side of the fuselage. Drill holes to fit the bearing in the supports. Use holes from plan as a guide. Test fit the bearings and carbon rod for alignment. Adjust holes as need. Once aligned glue bearings in with epoxy while rod is still in place. Careful not to glue rod to bearings.

Once bearings are dry remove rod and sand it where the control horn and end bearing will be glued. Insert rod partly from left side and slide on control horn. Push the rod through, past the motor mount and side on the end bearing. Install servo and push rod to control horn. Align all parts even and square then glue horn and end bearing in place with epoxy.

Cut access hatch in fuselage bottom for electronics. Tape out the hatch and cut at a 45 degree angle through the middle of the tape. Scotch tape will hold hatch closed after painting.

Glue on the fuselage top.

Sand completed fuselage to its final shape.

Sand stabilizer leading and trailing edges to a round (leading) and tapered(trailing)

edge. Then glue the stabilizers to the carbon rod with epoxy making sure they are aligned with each other.

Bluecore note: trim 1/8” of the film from each edge before sanding. Wrap the edge with scotch tape to protect.

Sand wing leading edge to a rounded contour. Cut slots in wings 3/4 into foam for carbon spars. Glue spars into wings and add spar reinforcement piece. Sand each trailing edge of the flaperons to a taper. Cut a 45 degree bevel on the leading edge of each flaperon with a ruler. Hinge one flaperon with a strip of scotch tape on the top. Fold flap up on top of wing flat and add another piece around the joint for the bottom of the hinge.

Bluecore note: trim 1/8” of the film from each edge before sanding. Wrap with tape.

Insert wing. Align and glue in place. Attach second flaperon with tape.

Sand vertical stab leading and trailing edges to a round (leading) and tapered(trailing)

edge. Center and glue vertical stab making sure it is at 90 degrees to the wings and stabilizer.

Bluecore note: trim 1/8” of the film from each edge before sanding. Wrap the edge with scotch tape to protect.

Use watered down Light drywall spackle to fill any gaps or rough spots.

Repair damage done from your dog jumping up to say hi!   DOH!

Back where we started.

Sand all surfaces smooth with very fine paper.

Spray a coat of Light Gray Metallic.

Tape off and paint trim with bright red.

Cut in panel lines with a butter knife and add decals.

Cut an exhaust nozzle from a foam coffee cup and paint. Trim and install around motor mount.

Install flaperon servos and radio equipment.

Install motor, prop and the rest of the electronics.

Prop saver recommended.

Assemble the drop tank/ bomb. Landing gear can be made for static display as an option.

Drop tank can be attached

with thin wooded dowels inserted through small holes in the bottom of the fuselage. Use a ½ long aluminum tube that fits the front gear dowel as a bearing support in the bottom of the front fuselage.

Add final paint details.

Whoa la!